## Slide 1
ITA0504
COMPUTER VISION
Analog vs Digital
Image Acquisition
NIHARIKA GUPTA
(192425013)

## Slide 2
INTRODUCTION
How Machines Come to See
1
Image acquisition: the first stage of any computer vision pipeline — converting a real-world scene into a form a system can process.
2
Two families of methods: analog acquisition (continuous physical signals) and digital acquisition (discretized, numeric pixel data).
3
Why it matters: acquisition quality directly bounds every downstream task: filtering, detection, recognition.
Scene
→
Sensor
→
Signal
→
Image
02

## Slide 3
Analog Image Acquisition
Light intensity is captured and stored as a continuous, unbroken physical signal — no numeric sampling involved.
Continuous signal in both space and amplitude
Captured on physical/chemical media (film) or as a varying voltage (video tube)
No pixel grid — infinite theoretical resolution, limited by media grain/optics
Degrades with copying, storage and time (fading, noise)
Requires digitization (a scanner/frame grabber) before computer processing
SIGNAL VIEW
Continuous voltage / intensity — smooth, unbroken curve
EXAMPLES
• 35mm film cameras
• Vidicon TV camera tubes
• X-ray film radiography
• Analog CCTV / VCR tape
03

## Slide 4
Digital Image Acquisition
The scene is sampled at discrete spatial points and quantized to finite intensity levels, producing a numeric pixel array.
Discrete signal — sampled in space, quantized in amplitude
Captured directly by CCD / CMOS image sensors as electronic charge
Fixed pixel grid: resolution defined by sensor array (e.g., 4000 × 3000)
Losslessly copyable and directly processable by algorithms
Ready for storage, compression, transmission and computer vision tasks
SIGNAL VIEW
Discrete grid of pixels — each with its own numeric value
EXAMPLES
• DSLR / smartphone cameras
• CCD & CMOS sensor arrays
• Digital X-ray & MRI scanners
• Webcams and IP cameras
04

## Slide 5
THE DIGITIZATION BRIDGE
From Continuous Scene to Digital Image
1
Sensing
Optical sensor (CCD/CMOS) converts incoming light into an analog electrical signal proportional to intensity.
→
2
Sampling
The continuous signal is measured at discrete spatial locations — fixing image resolution (rows × columns).
→
3
Quantization
Each sample's amplitude is mapped to the nearest of a finite set of intensity levels (e.g., 0–255).
→
4
Digital Image
Result: a 2-D array of integers — the digital image, ready for storage and processing.
05

## Slide 6
Analog vs Digital — At a Glance
Parameter
Analog Acquisition
Digital Acquisition
Signal type
Continuous in space & amplitude
Discrete (sampled & quantized)
Storage medium
Film, magnetic tape, photographic plate
Memory chips, SSD, cloud storage
Resolution limit
Bound by optics / film grain
Bound by sensor pixel count
Noise over copies
Accumulates with each generation
No degradation on copying
Processing
Needs a scanner/digitizer first
Directly computer-processable
Editing / transmission
Difficult, physical handling
Instant, algorithmic, networked
Typical devices
Film camera, vidicon tube
DSLR, smartphone, CMOS sensor
06

## Slide 7
Photographing the Same Scene, Two Ways
ANALOG PATH
1
Scene light exposes silver-halide crystals on 35mm film
2
Latent image formed as a continuous chemical gradient
3
Film is chemically developed in a darkroom
4
Printed onto photographic paper or scanned to view
DIGITAL PATH
1
Scene light hits a CMOS sensor's photosite array
2
Each photosite outputs a voltage proportional to light
3
On-chip ADC samples & quantizes into pixel values
4
Stored instantly as a JPEG/RAW file for viewing/editing
07

## Slide 8
Advantages & Limitations
Analog
Simple optics — no complex electronics needed to capture
High dynamic range — film can capture wide light ranges naturally
Degrades over time — fading, scratches, generation loss on copies
Slow workflow — developing & digitizing needed before use
Not machine-readable — cannot be directly processed by algorithms
Digital
Instant processing — directly usable in computer vision pipelines
Perfect copies — no quality loss on duplication or transmission
Easy storage & search — compact files, searchable metadata
Finite resolution — limited by sensor pixel count & bit depth
Sensor noise — quantization & thermal noise at low light
08

## Slide 9
Where Digital Acquisition Powers Computer Vision
Medical Imaging
Digital X-ray, CT & MRI enable direct algorithmic diagnosis support
Autonomous Vehicles
CMOS camera arrays feed real-time object & lane detection
Surveillance & Security
IP cameras stream digital frames for face & motion recognition
Industrial Inspection
High-res sensors detect defects on production lines
Remote Sensing
Satellite digital sensors capture multispectral earth imagery
Mobile Photography
Smartphone CMOS sensors enable computational photography
09

## Slide 10
Key Takeaways
1
Analog acquisition captures continuous signals on physical media; digital acquisition samples and quantizes into a numeric pixel array.
2
Digitization (sampling + quantization) is the essential bridge that makes any scene usable by a computer vision system.
3
Digital acquisition dominates modern computer vision — direct processability, lossless copying, and networked transmission are decisive advantages.
4
Analog methods persist where their unique optical properties (dynamic range, archival texture) are still valued.
10